## Slide 1
Hands-on Bluetooth with CYW20719 and its peripheral Capabilities
Ranjith Kumar, Kishor Palleti, Pooja Gedupudi
1st February 2020

## Slide 2: 80% of the final exam will be based on one of the lecture you missed and the one book you didn’t read 

## Slide 3: Agenda
Few Case Studies of Electronic Systems
Introduction to RF System-On-Chips (SoCs)
Overview of CYW920719Q40EVB-01 Evaluation board
Basics of Bluetooth and Bluetooth Low Energy
Basics of Wiced Studio IDE
CYW20719 Features
CYW20719 Peripherals
  Device Architecture
  System Resources and Peripherals
  Low Power Modes
Writing your first Bluetooth application on CYW20719

## Slide 4: Case Studies of Electronic Systems

## Slide 5: Simple Overview of Supply Chain in Electronics Industry

## Slide 6: Players (Same Firm may play in different business units)
IC Fabs: TSMC, Samsung, UMC, Global Foundries, Cypress., etc.
IC Packaging: ASE Technology Holding, Amkor Technology, JCET, SPIL., etc.
Fab Machines: KLA Tencor, Applied Materials, ASML., etc.
IC Design: Cypress, AMD, Intel, Samsung, QCOM, TI, NXP, Infineon, Xilinx, Lattice, SignalChip., etc.
EDA: Cadence, Synopsys, Mentor Graphics, AutoCAD., etc.
Instrumentation/Mathematical Analysis: National Instruments(AWR Corporation), Mathworks, Ansys, Keysight, Agilent, Rohde & Schwarz, Teledyne Lecroy., etc.
Consumer Elec. : Fitbit, Garmin, Philips, Amazon(Lab 126), Western Digital., etc.
OEMs/ODMs: Apple, Samsung, Nokia, Huawei, Compal, Westron, Foxconn., etc.
Distributors/Module Vendors: AVNET, Arrow, Digi-key, mouser., etc.

## Slide 7: Players (Continued…)
PCB Manufacturers/Services: Flextronics, Sanmina, OSHPark, design-spark, JLPCB, PowerPCB., etc.
Automotive: Bosch, Harman, Continental AG, Volvo, MB, Audi., etc.
Industrial/Robotics: Siemens, ABB, Schneider electric, General Electric., etc.
Aerospace/Defense: Boeing, Airbus, Bombardier, ISRO., etc.
RTOS/OS Development: Microsoft (ThreadX), Android (Linux Kernel), VxWorks, ENOS., etc.
NW/BB Provider: Alcatel, Cisco, Juniper, Huawei, AT&T, Nokia, ., etc.

## Slide 8: Facts about Cypress Semiconductor
Started in Silicon Valley by Dr. T. J. Rodgers in 1982.
Best Known for
  PSoC (Programmable System on Chip) Microcontrollers
  Memory Technologies (SRAM, FRAM, MRAM, Flash Memories)
  Sensing chips (Capsense, Magsense)
  USB, Power Management ICs and wireless charging Products
  Automotive Microcontrollers, clocks and buffers
  IoT Products (Bluetooth, WiFi and Combo devices)
Cypress stands No.1 in USB-C markets, WiFi and Bluetooth Combo device markets, Auto Cluster MCUs, Touch and NOR Flash markets.

## Slide 9: Smartwatch - Fitbit Charge 3

## Slide 10: Amazon Echo Connect

## Slide 11: Nintendo Switch

## Slide 12: Automotive Systems

## Slide 13: Quiz 1
What is Moore’s law?
Which are some of the common inter-chip bus communication interfaces?
Why do most Wireless protocols use 2.4 GHz band?
Notes: ANS:
Moore's law is the observation that the number of transistors in a dense integrated circuit doubles about every two years.
I2C, SPI, CAN, LIN, SDIO, PCIe., etc.
ISM band

## Slide 14: Introduction to RF System-On-Chips (SoCs)

## Slide 15: Fabrication Technologies of RF Circuits

## Slide 16: Discrete Components vs IC

## Slide 17: Why do we need RF SoCs?
Replaces bulky and expensive waveguide and coaxial components with small and inexpensive planar components for smaller size, lighter weight, lower power requirements, lower cost, and increased complexity.
System-On-Chip solution as opposed to System-On-package Solution.
  Reduces BOM cost and PCB footprint size.
  More reliable circuits as opposed to 3rd party Front-end components
Tighter integration also means low power consumption
Relaxed Filter requirements
More processing on the digital domain compared to analog domain. This is advantageous for flexibility
RF SoCs further reduce the BOM cost

## Slide 18: RF Basics
Radio Frequency waves are generated by the device(RF ICs) and sent over the antenna as EM waves.
  RF signals : 300 KHz to 300 GHz ; Wave length: 1 Km –1mm
  Microwave signals: 0.3 GHz –300 GHz ; Wave length: 1 m –10mm
  Millimeter-wave signals: 30 GHz –300 GHz ; Wave length: 10 mm –1mm

## Slide 19: Overview of Wireless Communication System

## Slide 20: Typical RF Transceiver (More details)

## Slide 21: Important Elements of a RF System
PAs – Transmitters - Drive antenna with high power level
LNAs – Receivers - Sense small signal (amplify with low noise)
Mixers – Mixers perform frequency translation by multiplying two waveforms. Multipliers in the Time domain & Convoluters in the frequency domain.
VCOs - An RF oscillator must be designed such that its frequency can be varied(tuned) across a certain range.
Frequency Synthesizers - Helps VCOs correct the frequency output errors.

## Slide 22: Few Important RF Units & Parameters
RF design has traditionally employed certain units to express gains and signal levels.
dB vs dBm
  Voltage gains and Power gains are expressed in dB.
  The absolute signal levels are often expressed in dBm rather than in watts or volts. Used for power quantities, the unit dBm refers to “dB’s above 1mW.”
S parameters – Scattering Parameters
Smith’s chart characteristics

## Slide 23: Duplexing / Multiplexing
The simplest case of multiple access is the problem of two way communication by a transceiver, a function called “duplexing.”
Multiplexing is the process of simultaneously transmitting two or more individual signals over a single communication channel eg: cable or wireless.

## Slide 24: Multiple Access Techniques

## Slide 25: Modulation
Modulation refers to a process of turning information into (electrical) signals which are suitable for transmission.
Carrying the information in digital form offers many advantages over communication in the analog domain.
The digital counterparts of AM, PM, and FM are called “amplitude shift keying” (ASK), “phase shift keying” (PSK), and “frequency shift keying” (FSK), respectively .

## Slide 26: Example – Bluetooth classic Air Interface

## Slide 27: Protocol Stacks and application Firmware
All the baseband hardware and the MCUness of the SoC are controlled by the registers defined in the RTL.
Most of the bare-metal code for controlling the registers are written in assembly (depends on the core) and C. Memorizing assembly is not that necessary (This suggestion is not for academics).
Most of the protocol stacks are written in a way like a Finite State Machine(FSM) to aid event-driven programming and are mostly time-sensitive.
Firmware is a generic term and can represent any part of the code (code memory) that lies in any part of the memory such as ROM, Flash (internal and external).

## Slide 28: Some of the Wireless Protocols & their Standard Organizations
3GPP - 2G GSM/3G WCDMA/4G LTE(VoLTE) /5G
IEEE & WiFI Alliance - WiFi – a/b/g/n/ac/ax/p
Bluetooth SIG - Bluetooth- 2…5.x
Google - Threadx
ZigBee
WiGig
GPS/GLONASS/GNSS/Beidou/IRNSS
NFC

## Slide 29: CYW20719 Development Kits

## Slide 30: CYW920719Q40EVB-01 Evaluation board - Top

## Slide 31: CYW920719Q40EVB-01 Evaluation board - Bottom

## Slide 32: Overview

## Slide 33: Schematics of CYW20719 based RF FE on PCB

## Slide 34: Zoomed in Version

## Slide 35: Quiz 2
What are the difficulties of designing High frequency RF Circuits on a PCB?
Why do we require Power Management ICs?
List out the different types of Antennas used?
Notes: ANS:
Impedance Matching, Noise from other HF circuits as it behaves as Antennas
Different power rails are required. The power design of the device has multiple requirements for operation.
Loop antenna, Planar F-antenna, ceramic chip antenna(on a PCB)
Wire Antennas
  Short Dipole Antenna
  Dipole Antenna
  Loop Antenna
  Monopole Antenna
Log Periodic Antennas
  Bow Tie Antennas
  Log-Periodic Antennas
  Log-Periodic Dipole Array
Aperture Antennas
  Slot Antenna
  Horn Antenna
Microstrip Antennas
  Rectangular Microstrip Patch Antenna
  Quarter-Wave Patch Antenna
Reflector Antennas
  Flat-plate Reflector Antenna
  Corner Reflector Antenna
  Parabolic Reflector Antenna
Lens Antennas
Travelling-wave Antennas
  Long Wire Antenna
  Yagi–Uda Antenna
  Helical Wire Antenna
  Spiral Antenna
Array Antennas
  Two-Element Array Antenna
  Linear Array Antenna
  Phased Array Antennas

## Slide 36: Bluetooth Low Energy and its History
Bluetooth was formalized by BT SIG - 20th May 1998
Bluetooth Low Energy v4.0 – 30th June 2010
Bluetooth Low Energy v5.2 – with LE Audio - 7th January 2020
As an alternative to the Bluetooth standard protocols that were introduced in Bluetooth v1.0 to v3.0, BLE is aimed at very low power applications powered by a coin cell.
For comparison, Typically BLE consumed 0.01 – 0.5 W compared to Classic Bluetooth’s 1W of power.
Standards prior to v4.0 is referred as Classic Bluetooth.

## Slide 37: Bluetooth Low Energy (BLE 4.0 & above)
Uses 2.4 GHz ISM Band
  Industrial Scientific Medical band
  License Free – with certain rules
  2400 MHz to 2483.5 MHz
  RF Channels f=2402 + k * 2 MHz , k=0,…,39

## Slide 38: Why BLE?
Support of Low energy connectivity applications.
Expected to operate without a battery change for an extended period of time.
Support for very low data rates.

## Slide 39: BLE Stack Architecture

## Slide 40: Device Roles (Different terminologies)
Central can connect to many peripherals at the same time
Peripheral can connect to only one central at any one time.

## Slide 41: BLE Advertising and Data Channels – Physical Layer

## Slide 42: Discovery and Connection – Link Layer
Defines how two BLE devices communicate.
Defines Advertising, Scanning, Connecting, Packet Format
BLE protocol defines Advertiser and Scanner activities for discovering peers and getting into a BLE connection. For ex:
  A sensor application will typically Advertise when in the ON state and not in a connection. The sensor device will take a slave role once in a connection.
  The other side will typically Scan for Advertisers when in the ON state and not in a connection. This device will take the master role once in a connection.
Link Layer states are summarized in the specification as follows:
  Standby State
  Advertising State
  Scanning State
  Initiating State
  Connection State

## Slide 43: Link Layer State Machine

## Slide 44: L2CAP
  Segmentation and reassembly of packets
  4-byte header
  MTU (Maximum Transmission Unit)
    BLE 4.0 & 4.1 - 23 bytes
    BLE 4.2 & above – 247 bytes
  Protocol multiplexing
      0x0004: ATT Channel (usually used)
        0x0005: LE signalling
        0x0006: Security Manager

## Slide 45: Attribute (ATT) Protocol
Action to be taken (Read/Write/…) – Basically a command
  1-byte instruction opcode
  2-byte handle (ID of relevant service/characteristic/descriptor)
  Bluetooth 4.0 & 4.1
    MTU(Maximum Transmission Unit) size - 20-byte
  Bluetooth 4.2 & above – Link Layer changes for DLE allows for more throughput
    MTU(Maximum Transmission Unit) size - 244-byte

## Slide 46: Generic Attribute (GATT) Profile
Service framework which uses the Attribute protocol
Defines procedures and formats of services and their characteristics. What is it for?
  It specifies how the data is stored and exchanged once connected.
  Identifies Services, Characteristics and Descriptors
Profile dependency
Server – Has the data
    accepts incoming commands and requests from the client
    sends responses, indications and notifications to a client
Client – wants the data
    initiates commands and requests towards the server
    receive responses, indications and notifications sent by the server

## Slide 47: Service, characteristic, descriptor
GATT
Service1
Service2
Characteristic1
Properties: Read, Notify
Characteristic1
Properties: Read, Write
Descriptor1
Characteristic2
Properties: WriteWithoutResponse
Descriptor1
Descriptor2
Notes: GATT elements such as Services, characteristics and descriptors are contained by Attributes
GATT composed of 1 or more services necessary to fulfill a use case

## Slide 48: Service, Characteristic and Descriptor
Service - collection of data and associated behaviors to accomplish a particular function or feature
  16-bit SIG services: Battery, Heart rate, Immediate Alert, Tx Power
  128-bit UUID for custom services
  Collection of characteristics
  Primary Service
  exposes the primary usable functionality of this device
  discovered using Primary Service Discovery procedures
  Secondary Service
  service that is only intended to be referenced from a primary or another secondary service or other higher layer specification

## Slide 49: Service, Characteristic and Descriptor(continued)
Characteristic
  Holds a value: String, Int, Char…..
  Can take on multiple properties:
    Read: Central can read this value directly
    Write: Central can write/change this value and be notified if executed successfully
    WriteWithoutResponse: Central just “fire and forget”
    Notify: Central gets alerted if the value has changed
    Others: Broadcast, Indicate, SignedWrite, QueuedWrite, WritableAuxiliaries
  Collection of optional descriptors
Descriptor: usually optional
  Holds a value
  Used to describe a characteristic (meta-data)
  Special case: Client Characteristic Configuration Descriptor (0x2902)
    Usually automatically created for characteristics with “notify” property

## Slide 50: Profiles and Services
A Profile defines and describes the use of services necessary to implement a given Application.
Bluetooth SIG adopted examples:
  Heart rate Profile
    Heart Rate Service (HRS)
    Device Information Service (DIS)
  Proximity Profile
    Link Loss Service
    Immediate Alert Service
  Find Me Profile
    Immediate Alert Service

## Slide 51: Generic Access Profile (GAP)
Information advertised to central before connection
Name of peripheral
Is it connectable?
Supported features (services)

## Slide 52: BLE GAP Device Roles
Broadcaster
  An advertiser that is non-connectable.
  Ex: Temperature Sensor
Observer
  Scans for advertisements, but cannot initiate connections
  Ex: Temperature Display
Peripheral
  An advertiser that is connectable
  Operates as a Slave after connection
  Ex: Heart rate sensor
Central
  Scans for Advertisements and initiates connections
  Operates as a master in connections.
  Ex: Smartphone

## Slide 53: BLE connection procedure
Observer
Broadcaster
Central
Peripheral
Broadcasts advertisement packets (GAP)
2.5. Connection attempt
Connect success
Discover services
Services data (GATT)
Discover characteristics
Characteristics data (GATT)
1. Scanning
Advertising
2. Received advertisement packet (Stop here for beacon devices)
Connected success, stops advertising
3. Connect success,
now lets find out more
Send back services info
4. Services discovered, lets dig deeper
Send back characteristics info
5. Discovery completed, ready to use peripheral
Discover descriptors (usually optional)

## Slide 54: Link Layer Packet Structure - Protocol Data Units (PDUs)
2 Types:
  Advertisement Channel PDUs
  Data Channel PDUs
Bluetooth SIG introduced Data Length Extensions in v4.2 Specifications.
Increased throughput

## Slide 55: HCI – Host Controller Interface
Host gives commands to the controller over HCI
Can be a single-chip or dual chip solution.
To enable interoperability between host and controllers produced by different manufacturers.
Usually HCI UART or USB.

## Slide 56: OS / Device Compatibility

## Slide 57: Quiz 3
Where did the term “Bluetooth” come from?
Which are some of the most used profiles in Classic Bluetooth?
How can I design a BLE solution to reduce the interference with WiFi?
Notes: ANS:
Danish King Harold Bluetooth
A2DP, HFP, HID, SPP, AVRCP
Co-Existence Interface

## Slide 58: CYW20719 Support in Wiced Studio IDE

## Slide 59: Wiced Studio IDE
Wiced Studio™ software is a set of tools that enable you to integrate Cypress devices into your existing development methodology
Wiced Studio is an IDE based on Eclipse IDE that supports Cypress Wireless connectivity devices with the help Bluetooth SDK and WiFi SDK.
For the workshop, We’ will concentrate mostly on the BLE peripheral side.
For further learning on Classic Bluetooth, BLE Mesh and OTA, please refer to the Cypress Semiconductor Github repository on the theory and implementation of applications.

## Slide 60: A Glimpse of Wiced Studio

## Slide 61: Minimal Application – Hello World of Wiced Environment

## Slide 62: CYW20719 Device Architecture

## Slide 63: CYW20719 Block Diagram
Bluetooth v5.0, Basic Rate + Enhanced Data Rate + Bluetooth Low Energy and BLE Mesh
  Industry’s most widely deployed Bluetooth stack
  2-Mbps LE support
  2 MB ROM for Bluetooth stack, Mesh, Threadx and other key libraries to let most applications fit in small flash footprint
Ultra low power BLE
  BLE - 14 uA Tx @ 0 dBm and 122 uA Rx
High transmit power to achieve long range
  CYW20719 - 4 dBm Tx BLE mode and 0 dBm Tx in EDR
MCU Subsystem
  96-MHz Cortex®-M4
  512KB SRAM, 1MB Flash
Packages
  40-QFN 5x5 mm and 134-ball WLCSP 3.2x3.2 mm

## Slide 64: System Resources – Power Domains
Two power domains exist
  VBAT is used to power the core
  VDDIO is used to power the peripherals and GPIOs
Voltage range for both VBAT and VDDIO : 1.8-3.3V
This allows peripherals to work at a different voltage than the core and allows power saving

## Slide 65: System Resources - Clocks
High Frequency (HF) clock derived from external 24 MHz crystal
  PLL converts clock to 96 MHz
  96 MHz clock divided to various frequencies for different blocks
  ACLK0 and ACLK1 can be derived from 24-MHz HF clock or 1-MHz HF clock
  SPIs, UARTs, I2C clock derived from PTU clock which in turn derived from HF clock
Low Frequency (LF, marked as lhl_lpo32k) clock derived from external 32 Khz crystal or internal LPOs
  RTC sourced from LF clock
  PTU – Peripheral Transport Unit ACLK – Auxiliary clock
  HP-LPO – High Power LPO LP-LPO – Low Power LPO

## Slide 66: System Resources - GPIOs
Two types of GPIOs
  LHL GPIOs are general purpose GPIOs to route most of the peripherals
  Arm GPIOs are GPIOs for specialized functions like DEV_WAKE, HOST_WAKE
CYW20719 supports the following GPIO capabilities:
  Input / Output selection
  Pull-up / Pull-down selection
  Drive strength selection
  Hysteresis control
  Level / Edge triggered interrupt selection
Certain functionalities (for example ADC input) are supported only on specific LHL I/Os
GPIOs such as P26, P27, P28, and P29 supports higher current source/sink compared to other pins.
Package | LHL GPIOs | Arm GPIOs
CYW20719B1KWB9G (134-ball WLCSP) | 40 | 6
CYW20719B1KUMLG (40-pin QFN) | 22 | 2
Notes: *source/sink 8 mA at 3.3V and 4 mA at 1.8V
*P26/P27/P28/P29 sink/source 16 mA at 3.3V and 8 mA at 1.8V

## Slide 67: System Resources - GPIO SuperMux
Flexible mux functionality for LHL GPIOs
Most peripherals can be routed to any LHL GPIOs using supermux
Device configurator can be used to easily route peripheral signals to GPIOs
List of peripheral signals that can be “supermuxed” can be found in datasheet

## Slide 68: Peripherals - ADC
Single-ended switched-capacitor sigma-delta ADC with ENOB of 10 bits for general purpose measurements, and 12 bits for Audio* applications
ADC Inputs: (Cannot be supermuxed)
The following 15 pins can be programmed as ADC inputs in CYW20719B1KUMLG (40-pin QFN):
  P0, P1, P10-P11, P13, P16-17, P23, P28, P29, P33-P36, P38
The following 28 pins can be programmed as ADC inputs in CYW20719B1KWB9G (134-ball WLCSP):
  P0, P1, P8-P19, P21-P23, P28-P38
Voltages of VDDIO, VDD_CORE, ADC_BGREF, and ADC_REFGND can also be measured using ADC
APIs are available in : wiced_hal_adc.h
The wiced_hal_adc_init() function initializes the necessary registers required for ADC operation in DC measurement mode. The ADC needs to be re-initialized if it has been powered down in specific low-power modes
The wiced_hal_adc_read_voltage() API function allows the program to read the analog voltage from the ADC
* Audio mode is available only in CYW20819A1KFB1G package

## Slide 69: Peripherals - Pulse-Width Modulation
Six 16-bit Hardware PWM are available
Supports 2 clock sources:
  LHL Clock at 32 KHz
  ACLK1 at 24 MHz
Supports SuperMux Functionality
APIs are available in : wiced_hal_pwm.h
The wiced_hal_pwm_start() function configures, enables, and starts the PWM and also routes it to a preconfigured GPIO pin. This function takes in five parameters (i.e., channel, clock source, toggle count, initial count, and invert signal)
  The channel refers to PWM channels 0 to 5
  The clock source can be either LHL_CLK or ACLK1 (PMU_CLK)
  The toggle count refers to the number of ticks to wait before toggling the signal
  The initial count is the initial value of the register
  The invert signal can be either 1 or 0. If the invert signal is 1, the PWM output starts at logic HIGH and if the invert signal is 0, the PWM output starts at logic LOW

## Slide 70: Peripherals – Real Time Clock (RTC)
Supports a 48-bit RTC Timer running on 32 KHz Low Power Oscillator
Supports clock input from either an external or internal LPO
By default, the date and time are set to January 1, 2010 with a time of 00:00:00 denoting HH:MM:SS
APIs are available in : wiced_rtc.h
wiced_set_rtc_time() – To set the current time of wiced_rtc_time_t structure
wiced_rtc_get_time() – To get the current time of wiced_rtc_time_t structure
wiced_rtc_ctime() – To convert the current time value to string

## Slide 71: Peripherals - Application Timers
Based on 64-bit hardware timer with 1 MHz input clock
Multiple software timer instances can be created
Two modes of Operation:
  Periodic Interrupt Mode
    WICED_SECONDS_PERIODIC_TIMER
    WICED_MILLI_SECONDS_PERIODIC_TIMER
  Single-Shot Mode
    WICED_SECONDS_TIMER
    WICED_MILLI_SECONDS_TIMER
APIs are available in : wiced_timer.h
The wiced_init_timer() function initializes the timer. It allows you to specify the callback function to be invoked when the timer expires. This function also allows you to specify timer type that should be used.
The wiced_start_timer() function is used to start the count down. The wiced_stop_timer() function can be used to stop the timer.

## Slide 72: Peripherals - Inter-Integrated Circuits (I2C)
  I2C Master mode, Slave mode (driver support to be added in future)
  7-bit addressing mode, clock stretching as a master, Multi-slave operation
  SCL Clock Frequencies: 100 KHz (Standard), 400 KHz (Fast Mode), 800 KHz (Proprietary), 1 MHz (Fast Mode+)
  Supports SuperMux Functionality
  APIs are available in : wiced_hal_i2c.h
  The wiced_hal_i2c_init() function allows the user to initialize the I2C module register for I2C master mode of operations
  The wiced_hal_i2c_set_speed() function allows you to set the SCL clock frequency of the I2C block
  The wiced_hal_i2c_write() function writes data to a specific Slave address
  The wiced_hal_i2c_read() function reads data from a particular Slave address
  The wiced_hal_i2c_combined_read() function executes a write transaction followed by a read transaction with a repeated start condition between the transactions

## Slide 73: Peripherals - Serial Peripheral Interface (SPI)
CYW20819 contains 2 SPI Hardware blocks supporting both Master and Slave modes
Supports Super-Mux Functionality
Configurable SCK polarity, phase and frequency (upto 24 MHz clock)
Configurable LSB or MSB first transfer
APIs are available in : wiced_hal_pspi.h
The wiced_hal_pspi_tx_data() function is used to place the data in the TxFIFO to transmit the data as a Master
The wiced_hal_pspi_rx_data() function is used to receive the data as a Master
The wiced_hal_pspi_exchange_data() function can be used to send and receive data simultaneously as a Master
The wiced_hal_pspi_slave_tx_data() function is used to place the data in the TxFIFO to transmit the data as a Slave
The wiced_hal_pspi_slave_rx_data() function is used to receive the data as a Slave

## Slide 74: Universal Asynchronous Receiver Transmitter (UARTs)
2 UART Blocks : HCI UART and Peripheral UART (PUART)
  8-bit transfer up to 3 Mbps
  9-bit transfer including an additional stop bit at a transfer rate up to 2.5 Mbps
  Configurable flow control
PUART:
  Interrupt functionality on receive operation
  Supports Super-Mux Functionality
  Used for debug and external peripherals
  APIs are available in : wiced_hal_puart.h
  The wiced_hal_puart_init() function is used to initialize the PUART block.
  The wiced_hal_puart_write() function is used to send one byte via the TX line.
  The wiced_hal_puart_register_interrupt() function provides an interrupt callback on receive of data.
HCI UART:
  Used for HCI transport for controller mode and is also used for programming the device
  The HCI UART signals are fixed to specific I/O pads
  DMA is used for HCI UART packets when the length of the data to be received is greater than around 64 bytes
Notes: For receiving data, register an interrupt callback function, set the watermark to determine how many bytes should be received before an interrupt is triggered, and enable Rx. A code snippet for receiving data on PUART is given below.
wiced_hal_puart_register_interrupt(rx_interrupt_callback);
/* Set watermark level to 1 to receive interrupt up on receiving each byte */ wiced_hal_puart_set_watermark_level (1);
wiced_hal_puart_enable_rx ();
The Rx processing is done inside the interrupt callback function. The PUART interrupt must be cleared inside the callback function to receive additional characters.
void rx_interrupt_callback (void* unused)
{
uint8_t readbyte;
/* Read one byte from the buffer and then clear the interrupt */
wiced_hal_puart_read (&readbyte);
wiced_hal_puart_reset_puart_interrupt ();
/* Add your processing here */
}

## Slide 75: CYW20719 Low Power Modes
Active
Timed Wake
HID-
OFF
Idle
Sleep
ePDS
Application can force at any time
Property / Mode | Active | Idle | Sleep | ePDS | Timed Wake / HID-OFF
Clocks | All clocks active | HCLK at 4/8 MHz. Other clocks active | HCLK off, Other clocks active | Only LPO active | No clocks active
SRAM retained? | NA | Yes | Yes | Yes | No
Wake sources | NA | Any configured interrupt | GPIO, timer, BT activity | GPIO, timer, BT activity | GPIO, timer
Enter asynchronously? (without PMU intervention) | NA | No | No | No | Yes
BT activities | Everything allowed | Everything allowed | Everything allowed | Everything allowed. Minimum sleep time should be ~10 ms | Nothing allowed

## Slide 76: Peripheral State in Low Power Modes
Peripheral / Mode | Active | Idle | Sleep | ePDS | HID-OFF/Timed Wake
CPU | On | WFI1 | WFI1 | WFI1 | WFI2
SPI | On | On | On | Off | Off
I2C | On | On | On | Off | Off
HCI UART | On | On | On | Off | Off
PUART | On | On | On | Off | Off
ADC | On | On | On | Off | Off
TRNG | On | On | On | Off | Off
PWM | On | On | On | On | Off
Keyscan | On | On | On | On | Off
Timer | On | On | On | On | Off
GPIO | On | On | On | On | On
SRAM | On | On | On | Retained3 | Off
WFI – Wait For Interrupt. The CPU is sleeping and will wake up on an interrupt
WFI – Wait For Interrupt. The CPU will reset
3. Retained – The memory contents are retained but cannot be accessed in that state

## Slide 77: Power Management Unit and Software Flow
Software implementation with necessary hardware support
Execution from lowest priority thread aka idle thread
Implements low-power modes, transitions and timing
Implements wake ISR
Detect, switch and calibrate LPOs
Communicate with different blocks for entering low power modes
1 - The function name is application code implementation specific

## Slide 78: Steps to Add Low Power in User Application (1/2)
Add sleep header files
  wiced_sleep.h file must be included in the source code
  Contains the structures and API functions related to low-power operation of CYW20819
Set up sleep configuration
  Declare a global variable of type wiced_sleep_config_t
  Initialize all the elements of the structure just after stack initialization
  Call wiced_sleep_configure()
/** This structure defines the sleep configuration parameters to be passed to * wiced_sleep_configure API */ typedef struct { wiced_sleep_mode_type_t sleep_mode; /**< Defines whether to sleep with or without transport */ wiced_sleep_wake_type_t host_wake_mode; /**< Defines the active level for host wake signal */ wiced_sleep_wake_type_t device_wake_mode; /**< Defines the active level for device wake signal. If device wake signal is not present on the device then GPIO defined in device_wake_gpio_num is used */ uint8_t device_wake_source; /**< Device wake source(s). See 'wake sources' defines for more details. GPIO is mandatory if WICED_SLEEP_MODE_TRANSPORT is used as sleep_mode* uint32_t device_wake_gpio_num; /**< GPIO# for device wake, mandatory for WICED_SLEEP_MODE_TRANSPORT */ wiced_sleep_allow_check_callback sleep_permit_handler; /**< Call back to be called by sleep framework to poll for sleep permission */ }wiced_sleep_config_t;

## Slide 79: Steps to Add Low Power in User Application (2/2)
Create a sleep callback function
  PMU calls this function to ask application for sleep permission
  Takes one argument of type wiced_sleep_poll_type_t. Specifies the reason for the callback
    WICED_SLEEP_POLL_SLEEP_PERMISSION – Sleep allowed or not
    WICED_SLEEP_POLL_TIME_TO_SLEEP – Time to sleep
      Always pass WICED_SLEEP_MAX_TIME_TO_SLEEP
  Final decision to sleep entry depends on the PMU
Create wakeup events like timers
  Events needed to wake up from low power mode
    GPIO interrupt - wiced_hal_gpio_register_pin_for_interrupt() API to register callback on GPIO wake up
    Timer interrupt – Register application timer with the stack

## Slide 80: HID-Off/Timed-Wake
HID-Off and Timed-Wake mode can be entered at any time from the application
No permission required from the PMU
wiced_sleep_enter_hid_off() API function can be used to enter the HID-Off mode
  Specify the time to sleep, a GPIO pin to wake up from HID-Off, and the trigger polarity
  Make sure no Bluetooth activity is in progress when calling this API

## Slide 81: Power Numbers
Setup
Code example from CE225540 – Low Power Application
CYW920719Q40EVB-01 kit
VBAT measured across J8
VDDIO measured across J15

## Slide 82: Resources
Kits
  CYW920719Q40EVB-01 Evaluation Kit
Documentation
  CYW20719 Datasheet
  CYW20719 Low-Power Guidelines
  CYW20719 Product Guide
  Cypress Academy Wiced BT101 Class - Github

## Slide 83: Any Queries?
Thank You 